2. Mechanizm RBAC (ang. Role-Based Access Control)

Topologia i wstępna konfiguracja:

p4-4-3-role-based-cli-przed.pkt

Polecenia:

R1>enable
Password:
t
R1#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.

   włączenie AAA i ustawienie root i ustawienie root view

R1(config)#aaa new-model
R1(config)# exit

R1#enable view
Password:
R1#%PARSER-6-VIEW_SWITCH: successfully set to view 'root'.

R1#

R1#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.

R1(config)#parser view W1
R1(config-view)#%PARSER-6-VIEW_CREATED: view 'W1' successfully created.

R1(config-view)#
R1(config-view)#secret cisco1
R1(config-view)#commands exec include show
R1(config-view)#exit
R1#

R1#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.

R1(config)#parser view W2
R1(config-view)#%PARSER-6-VIEW_CREATED: view 'W2' successfully created.

R1(config-view)#secret cisco2
R1(config-view)#commands exec include ping
R1(config-view)#exit

R1#configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
R1(config)#parser view W3
R1(config-view)#%PARSER-6-VIEW_CREATED: view 'W3' successfully created.

R1(config-view)#secret cisco3
R1(config-view)#commands exec include reload
R1(config-view)#exit

write

R1#show running-config

   sprawdzenie widoków:

R1#enable view W1
Password:
R1#%PARSER-6-VIEW_SWITCH: successfully set to view 'W1'.

R1#?
Exec commands:
disable Turn off privileged commands
enable Turn on privileged commands
exit Exit from the EXEC
logout Exit from the EXEC
show Show running system information
R1#exit

R1>enable view W2
Password:
R1#%PARSER-6-VIEW_SWITCH: successfully set to view 'W2'.

R1#?

R1#reload
R1>enable view W3
Password:
R1#%PARSER-6-VIEW_SWITCH: successfully set to view 'W3'.

R1#?
Exec commands:
disable Turn off privileged commands
enable Turn on privileged commands
exit Exit from the EXEC
logout Exit from the EXEC
reload Halt and perform a cold restart
R1#

    sprawdzenie statusu widoku po wylogowaniu z widoku W3:
R1>enable
Password:

R1#show parser view
No view is active ! Currently in Privilege Level Context
R1#en

R1#enable view
Password:
R1#%PARSER-6-VIEW_SWITCH: successfully set to view 'root'.

R1#show parser view
Current view is 'root'
R1#?
Exec commands:
<1-99> Session number to resume
auto Exec level Automation
clear Reset functions
clock Manage the system clock
configure Enter configuration mode
connect Open a terminal connection
copy Copy from one file to another
debug Debugging functions (see also 'undebug')
delete Delete a file
dir List files on a filesystem
disable Turn off privileged commands
disconnect Disconnect an existing network connection
enable Turn on privileged commands
erase Erase a filesystem
exit Exit from the EXEC
logout Exit from the EXEC
mkdir Create new directory
more Display the contents of a file
no Disable debugging informations
ping Send echo messages
reload Halt and perform a cold restart
resume Resume an active network connection
rmdir Remove existing directory
send Send a message to other tty lines
setup Run the SETUP command facility
show Show running system information
ssh Open a secure shell client connection
telnet Open a telnet connection
terminal Set terminal line parameters
traceroute Trace route to destination
undebug Disable debugging functions (see also 'debug')
vlan Configure VLAN parameters
write Write running configuration to memory, network, or terminal
R1#